## Slide 1
CAMBRIDGE INTERNATIONAL PROJECT QUALIFICATION · PROPOSAL DEFENSE
S-curve vs. PID
Energy, Time and Differential Suppression for a Two-Motor Robot Car
“Which control strategy moves my robot car faster and cheaper — and which one keeps it straight?”
[Your Name] · Centre CN213, Shanghai Guanghua College · Series 06/27
August 2026

## Slide 2
AGENDA
Outline
2 / 12
01
Background
& Motivation
why this question
02
Experimental
Design
variables · protocol · metrics
03
Feasibility
platform · skills · risks
04
Timeline
Aug 2026 → Apr 2027
Total: 7–8 minutes · 12 slides

## Slide 3
01 · BACKGROUND & MOTIVATION
The Problem I Met
3 / 12
• Built a two-motor robot car — ESP32 + encoder motors, my own hardware
• Observation 1 — motors are the biggest power consumer: the battery drains quickly and much of the energy is wasted rather than converted into motion
• Observation 2 — same PWM ≠ same speed: the two wheels differ by ~5% (wheel encoders) due to motor manufacturing differences → the car drifts off a straight line
• Question raised: does how we command the motors change the energy cost and the accuracy of the movement?
[ photo: the robot car ]
[ plot: rpmL vs rpmR diverging ]
replace before the defense

## Slide 4
01 · BACKGROUND & MOTIVATION
Two Ways to Command a Motor
4 / 12
S-curve motion profiling (open loop)
• Speed follows a smooth, jerk-limited S-shaped reference
• Standard in CNC machines & industrial robots — limits vibration and mechanical stress
Nguyen et al. 2008 · Meckl et al. 1998
PID feedback control (closed loop)
• Continuously corrects PWM from the measured speed error (encoders)
• Most widely used control algorithm in industry
Åström & Hägglund · Mahmud et al. 2020 · Hammoodi et al. 2020
Key structural difference: an open loop sees nothing — a closed loop corrects.

## Slide 5
01 · BACKGROUND & MOTIVATION
Research Gap & Research Question
5 / 12
• Gap — most published comparisons are simulation-based with a single idealised motor: no mismatched motors, no battery, no energy data
Q1 Which strategy completes the task with less energy?
Q2 Which one settles at the target speed faster?
Q3 How much differential can only PID remove?
RESEARCH QUESTION
“How do S-curve open-loop motion profiling and PID closed-loop control compare in the electrical energy consumed and the time taken to complete a speed-change task on a self-built two-motor robot car — and to what extent can PID control additionally suppress the wheel-speed difference that open-loop control cannot solve?”

## Slide 6
02 · EXPERIMENTAL DESIGN
Test Platform & Measurement
6 / 12
HARDWARE
• ESP32 controller
• 2 × JGB37-520B encoder motors (330 counts/rev)
• DRV8833 motor driver
SENSING & LOGGING
• INA226 — bus voltage, current, electrical power
• MPU6050 gyroscope — yaw rate (independent turning check)
• Telemetry @ 10 Hz → CSV: target, rpmL, rpmR, PWM, gyrZ, V, I, P
ALREADY RUNNING
Dual-wheel PID @ 100 ms · anti-windup · optional feed-forward — firmware tested on the real car
TO ADD
On-board S-curve reference generator for the open-loop mode — the same car then runs both strategies

## Slide 7
02 · EXPERIMENTAL DESIGN
Variables & Experimental Protocol
7 / 12
INDEPENDENT
control strategy: S-curve open-loop vs. tuned PID
DEPENDENT
energy (J) · settling time (s) · rpmL−rpmR · yaw rate
CONTROLLED
same car, surface, battery window, speeds · ≥3 repeats
Exp | Design | What it tells us
A | Same speed-change task under both strategies | the energy & time comparison
B | Step-response measurement | system dynamics
C | One-factor-at-a-time PID tuning (Kp, Ki, Kd, FF) | fair tuning — PID not misrepresented
D | Identical S-curve commands vs. per-wheel PID | differential suppression (unique to feedback)
E | Robustness across target speeds (15 / 45 / 90 rpm) | how far conclusions generalise
Extension: PID tracking an S-curve reference — the best of both worlds?

## Slide 8
02 · EXPERIMENTAL DESIGN
Metrics & Hypotheses
8 / 12
HOW THE WINNER IS JUDGED
• Energy = ∫P dt — INA226 power sampled at 10 Hz, integrated over the task
• Settling time — from command until speed stays within a ±5% band of target
• Analysis — mean ± SD over ≥3 repeats, plots in Python / Excel
H1 PID settles faster but may overshoot; the S-curve is smooth by construction
H2 The energy outcome is genuinely open — that is why it must be measured
H3 PID drives rpmL−rpmR → ~0; open-loop leaves ~5% → the car keeps drifting

## Slide 9
03 · FEASIBILITY
Platform & Data Pipeline Already Work
9 / 12
• Hardware: built, wired and running — tested wiring checklist v3.3
• Firmware: PID, telemetry and CSV logging already produce real data (test runs completed in August)
• Remaining build work: one S-curve generator function — weeks, not months
• Low cost, common components → quick repair or replacement
• Supervisor support for the experimental design and review
[ screenshot: real CSV telemetry curve ]
replace before the defense

## Slide 10
03 · FEASIBILITY
Skills, Risks & Backups
10 / 12
Skills in hand: Arduino / ESP32 firmware · Python (pyserial, pandas) · PID theory (Åström & Hägglund)
Risk | Mitigation
INA226 sensor drops out | firmware auto-reconnect + multimeter cross-check
Battery voltage drifts | fixed voltage window per session + voltage logged every sample
Encoder quantisation noise | 100 ms sampling period, low-pass filter, ≥3 repeats
Schedule slip | 6-week buffer before submission
Ethics & safety: low voltage (≤9 V) · bench-tested · new behaviours always wheels-off-ground first

## Slide 11
04 · TIMELINE
Aug 2026 → Apr 2027
11 / 12
Phase | Time | Deliverable
S-curve generator + pilot tests | Aug – mid Sep 2026 | tested open-loop mode
Main experiments A–E + repeats | mid Sep – Nov 2026 | complete CSV dataset
Extension: combined strategy | Nov – Dec 2026 | extra dataset
Data analysis + literature write-up | Dec 2026 – Jan 2027 | figures + review section
Report writing | Jan – Feb 2027 | first full draft
Revision + supervisor review | Mar 2027 | second draft
Buffer + proofreading + submission | Apr 2027 | final report (06/27 series)
Every phase ends with a concrete deliverable — slippage becomes visible early.

## Slide 12
SUMMARY
Expected Contribution
12 / 12
• Same car, same task, two strategies — measured, not assumed
• Two outcomes: the energy–time trade-off + quantified differential suppression that only feedback provides
• Deliverable: evidence-based guidance for battery-powered robots, with an open dataset from a fully documented platform
Thank you — Questions?